## Slide 1
Notes: Introduction to Brain Injury survivor Todd Westley

## Slide 2
This presentation is publically available on github:
https://github.com/toddwestley/Arduinos-to-turn-equipped-bike-into-Joystick-with-throtle-axis so you can download these slides.
Summary: In my humble opinion, riding a bike trainer is mind numbing.
Playing a flight simulator (without warping time) is equally mind numbing.
In combination, they lead to a palatable activity for me.
        I discovered that I could play games in plain sight of those around and they incorrectly conclude the activities are only exercise.
        I now can plan the nature of my exertions, i.e. how fast can I climb that hill?, and include variations from real world weather.
        This presentation is about my quirky leisure activity.
Notes: Slides that I thought about sharing are still there in case you ask me about something I already thought of.
What time warping?
1 hour flight could only require 15 minutes
I spite of disability, I still can enjoy cycling.

## Slide 3
It all began when my Uncle Steve was building a Piper cub from scratch while I lived in Ohio. In the winter, it was too cold for me to ride my bike outside. I rode a trainer, but it was boring. Than I decided to couple that with playing a flight simulator that had a piper cub aircraft. I used as USB-1208LS to capture the speed of my rear wheel and translate that into a throttle position. At that point, I got in the habit of virtually flying.
Notes: Flying without flight lessons or a pilot’s license is not unheard of.
Ask he flew without even a single lesson?

## Slide 4
My configuration worked for me; but, no one knew about the bike trainer hardware / software I used.
After moving back home, I sought to revive this technology and improve upon it so it could be shared with others.
Above: link to FlightGear
Notes: TBI
Quiz follows for three reasons
Ohio PEs that watch a webinar to attain CEUs are
required to pass a quiz
A quiz identifies what I hope you learn
I am envious of other professionals to attain CEUs
at this conference
Lately, I concentrate on improving my cycling cadence
Plus, my mind improves: I use mental energy to complete virtual flights.
If nothing else, it is more interesting to hear about my virtual flights than my time on the bike trainer
Uncle Steve??
Need to fix link to article

## Slide 5
Details: Playing a flight simulator with a joystick with a throttle axis is better than
just using a keyboard and mouse.
Throttle axis
Notes: I enjoyed playing FlightGear so I purchased a flight stick…
That was not satisfactory to me

## Slide 6
Details: I knew a bike on a trainer could be used to control the throttle axis.
Bike on trainer; sweat guards in place.
Sweat guards prevent corrosion.
I have already replaced the bottom bracket twice!
Notes: I try not to sweat;
Sweat guards prevent damage to your bike

## Slide 7
Details: How could could the speed sensor on the rear wheel be used?
Speed sensor
A speed sensor is required! Above is a link to Amazon.com
Notes: Amazing to me, I kept an o-ring from years ago (when I worked with hydraulic crimp tools for plumbing systems, I think) that was ideal for sensor installation on my rear wheel ultegra hub
Initially, the sensor only work with a cell phone app. But, again, I was not satisfied. I knew I could do better.

## Slide 8
Details: When the wheel is spinning, the speed sensor transmits, with blue
tooth low energy, information on the total number of spins and angular
speed of the last spin.
Here is an 8 byte transmission (that occurs every second unless the
speed sensor stops spinning for 2 minutes) [going forward, the
transmitted information will be referred to as an array of 8 unsigned bytes called rawValue]:
1 ,5 ,16 ,0 ,0 ,182 ,82 ,0
The total number of rotations is the sum of
The “last event”
8
182+20992=21174
5+4096+0+0=4101
Total rotations
Last Event Time
Notes: 8 bits to a byte…
I think the transmission is in reverse IBM form
I learned this while using a linux based Raspberry PI – I use linux OS; not Windows. But my scheme still works for Windows users.

## Slide 9
Details: Merely, capturing this stream of bytes filled the programming space of an Uno
WiFi Rev2 Arduino.
A second Arduino is required.
Note: The BLE signal from the speed sensor must be read by a sensor no
more than arms length away.
Notes: 2nd Arduino Leonardo acts as the joystick…
Source code available on github.

## Slide 10
What is an Arduino?
From “opensource.com”:
In a nutshell, an Arduino is an open hardware development board that can be used by tinkerers, hobbyists, and makers to design and build devices that interact with the real world.
Notes: Here is a description of an Arduino

## Slide 11
Details: These 8 bytes of information are transmitted via the wire interface
(using the ground, SCL [serial clock], and SDA [serial data] pins) to an
Arduino Leonardo that can act as joystick.
Notes: Leonardo and Uno Wifi Rev2 shown. Note the wires to channel information from the uno to the leonardo
I am not gifted at physical skills…this is the way I use it.

## Slide 12
I put a lot of thought into how this works. Speed on the trainer translated linearly from your unchanging maximum speed to zero, right? That is not what you are going to see! Ask to see my math-centric explanation.
You’ll have to ask me or download the slides from github to see my thoughts.
This diversion brought back the enjoyment of cycling to me. It brought variations from winds, temperatures, and altitude into the basement. I also enjoy programming and relearning math. [from a high school junior, Gabe Wu]
It’s not about physical fitness although that is a side effect. Note, during the COVID-19 I was out breath (and even today) and my habit leads in increased body temperature and muscle soreness. (all COVID symptoms) The activity, I believe, also led to a low resting heart [bradycardia] rate (52 bpm).

## Slide 14
Questions?
And/or
Watch Todd fly virtually from KGAI to KBWI [About 16 minutes]

## Slide 15
Heading
Altitude above ground
Altitude above sea level
Rudder (auto-
coordination
in use)
GPS destination
Throttle
Air speed (knots)
Aileron (and trim)
Elevator (and trim)
Glide slope
Notes: Heads Up Display

## Slide 16
I am in debt to the Holy Spirit for gently encouraging me to move forward on this project.
If you are moved, please make a donation to:

## Slide 17
Possible questions:
  Did you make a quiz so Ohio PE’s could earn a CEU?
  Can you better illustrate/explain the math involved?
    Could have used a Laplace transform?
  Can you explain the parameters that dictate the throttle position?
  Did you know trainer resistance fades during their use? Did you take this into account?
  How do turn on/off the glide slope indicator?

## Slide 18
Quiz:
An Arduino is?
A. Small lizard indigenous to Northern Mexico
B. Hardware development circuit board
C. An alternative to salt-peter
D. Slang for a nerdy middle school student
The stream of data from a speed sensor is made up of how many bytes every second?
A. 8
B. 1
C. 64
D. 2
How many Arduinos did Todd use to transform a bike trainer into a joystick throttle axis?
A. 0
B. 1
C. 2
D. 16
What pins are used by the Arduino “Wire” library
A. SDA
B. SCL
C. Ground
D. All of the above
Notes: C
B
C
D

## Slide 19
Quiz:
At most, how manty bits of the speed sensors’ transmission are used by Todd’s Arduinos every second?
A. 64
B. 6
C. 7
D. 8
How many bit comprise the “last event” evaluation to determine cycling speed?
A. 2
B. 4
C. 8
D. 12
Who determines when it is necessary to operate the bike’s shifters?
A. The end user decides.
B. The end user is given suggestions by the Arduino.
C. The Arduino wire library dictates this to the cyclist
D. The shifters operate through BLE
Notes: B
B
A

## Slide 20
Quiz:
According to Todd, using a bike trainer by itself is:
A. Mind-numbing
B. Exhausting
C. Critical for improving short-term strength
D. Furniture, similar to a couch
The units of “speed gradient”, if distance traveled is miles, are:
A. millimeters
B. miles per hour
C. miles
D. unit less
The exponential function used by Todd to determine what the cyclists’ speed should be is:
Notes: A
C
A

## Slide 21
Details: This is very math centric…Formulas used in the Arduino programs I authored include:
Constants
“RawValue” description
Speed calculation
Joystick throttle axis position calculation
Notes: What follows in math intense….It took me 6+ years to get here. Frankly, I would have reviewed this presentation numerous times if it had been available.

## Slide 22
based on the type of tire. This for a 700CC X 23mm road tire
This the highest speed you could theoretically obtain after operating the trainer for a long time
You pick this constant…help follows
This is the highest resolution possible
Notes: Constants
Wheel circumference can be found internet.
Note: I try to state units explicitly – this is a trick I used to pass the PE examination to eliminate incorrect answers on the multiple choice portion of the test.

## Slide 23
previous
Notes: Total rotations from rawValue

## Slide 24
or
Notes: Speed calculation
Delta wheel event must be positive

## Slide 25
*speedDelta+maxSpeed
Notes: Joystick throttle position calculation

## Slide 26
This is nerdy, and I am pretty sure the Arduinos are working even if their serial outputs are not visible, but, I like to know they are working (and how hard I am working the bike) while playing FlightGear so I wrote this Linux script.
You can also use the serial monitor on Arduino IDE to view the output from the Arduino Leonardo.
Notes: I use Linux; it is possible to do this on Windows.

## Slide 27
How are SpeedGradient, SpeedDelta, and MaxSpeed defined?
I found something that worked for me…. Below is a link to a spreadsheet
You can adjust the parameters in cells L2:L3 see how they impact an actual ride (blue dots) from their use (red line). You can copy the contents to a new sheet and replace data in column A from one of your actual rides.
Notes: I made an Excel worksheet so you can determine your own Speed Gradient, SpeedDelta, and MaxSpeed.

## Slide 28
Details: Why use an exponential function?
Think of your effort on the bike trainer as a stream of water. Think of
your bike trainer as a tank for that water. That tank has a small hole at
the bottom. Water leaves that tank at a rate proportional to its height. As
time goes on, the tank will reach a constant level. That water (trainer
temperature) represents the resistance of your trainer. As time passes, the
resistance decreases and you pedal faster. This produces a differential
(i.e. difficult) equation whose solution includes an exponential function.
https://www.youtube.com/watch?v=-1ARYph3mNA
Notes: I used a high school junior to help me solve a differential equation equivalent to understanding water flow into a tank (with constant cross-section) with a hole at its bottom.
I put much thought into using a decaying exponential function.

## Slide 29
I am in debt to the Holy Spirit for gently encouraging me to move forward on this project.
If you are moved, please make a donation to:

## Slide 30
Thing left to do:
add slides to show how to define speedDelta, maxSpeed, speedGradient
what is an Arduino?
make a quiz
make a box for Arduinos
order USB cables
email Bryan Pugh about presenting next year
offer CEUs to other PEs
oring for speed sensor
Annex
What I did to make flightgear run on Windows two – DLLs
vcruntime140_1.dll
msvcp140.dll
Windows CoolTerm vs Linux script to record Serial Output of Leonardo
Comparison of joystick set up
spellung error on github

## Slide 31
Cost Analysis for potential end user
Assumptions: Potential users have a bike only and will consider Windows 10 PC only.
Amazon or McMasterCarr will be sole source of products
Potential users have space for this stuff:
Trainer stand 34.99
Desktop PC w/ Monitor 131.50
Arduino Leonardo w/cable 14.99
Arduino Uno Wifi Rev2 (abx00021) 54.96
Wahoo Speed Sensor 39.99
Fan 39.99
4 port USB port w/ power switches 16.95
Keyboard cover *must match PC’s keyboard! 13.99
Trainer Sweat Guard 9.99
80/20 Material to make shelf to go over handle bars 234.75 Arduino Jumper Wires [you should be able to find these!] 1.99
USB cable for Arduino Uno 6.99
Total 651.08+shipping
Green from McMaster Carr

## Slide 32
234.75

## Slide 33
Wow, $651.08 + shipping! I thought Todd had a fixed income.
I rode a trainer stand, prior to Oct 29, 2014. After that day I rode that a trainer stand for a few weeks before I severed the shaft leading to the trainer stand’s fly wheel. I also used that trainer to control the throttle axis with a USB-1208LS. I already had an affinity for the Linux PC I have – I was frugal and liked to program.
Arduino are open source and appeal to hobbyists: I challenge you to find a more economical alternative.
Cheaper ANT+ speed sensors are available. I am unwilling to deviate.
In Elyria, I kept my apartment at 55°F – the furnace was loud; the lease did not allow me to go lower. When I moved back home, other residents preferred a warmer temperature. I try not sweat.
I did not know how to find a shelf: I built one from materials I knew about. Surely you can find a cheaper alternative.
From the USB-1208LS, I had a type B USB cable for the Arduino Uno Wifi Rev2
I have oodles of jumper wires: if you need some, come by my residence and I will give you some.

## Slide 36
Comparison of Joystick configurations – Windows, Microsoft takes credit.

## Slide 37
Comparison of Joystick configurations – Linux, Arduino LLC takes credit

## Slide 38
What I did to make FlightGear run on Windows – two missing DLLs
vcruntime140_1.dll -- followed instructions on YouTube
msvcp140.dll -- found on hard drive and copied
into FlightGear directory
If I did this over again, I would install and run CoolTerm first, then FlightGear

## Slide 39
I like to see and have a record of the Serial Output from the Leonardo. On linux, I use this script file
[batch file]:
PREFIX=Arduino_from_20
SUFFIX=.txt
TIMEDATENOW=$PREFIX$( date +%y_%m_%d_%s)$SUFFIX
stty -F /dev/ttyACM0 raw 9600
cat /dev/ttyACM0 2>&1 | tee $TIMEDATENOW
The same can be accomplished on Windows by using CoolTerm…

## Slide 40
Download and install coolterm
launch cool term
click options
Select Leonardo port
you can learn this from the
Arduino IDE
Click fonts
change font size to as desired

## Slide 41
Click connection menu >> capture to Text/Binary File >> start

## Slide 42
Select a name as prompted…
Click connect
Plug USB cable into Uno Wifi Rev 2 Arduino (this causes the Arduino to restart)
Start FlightGear, select departure airport, etc. …get past launcher,
after cockpit is visible… Start pedaling – Serial Output data will appear,
When ride is complete…
Unplug the Uno Wifi Rev 2
Connection >> Capture to Text/Binary File >> stop
Disconnect Serial
Quit – Don’t save settings
If desired, analyze the ride to (Select topSpeed, deltaSpeed, and speedGradient)