## Slide 1
Before I was hit by a van, I flew virtually during the Ohio winters by controlling the throttle of FlightGear with my bike on a trainer.
My configuration worked for me; but, no one else knew about the bike trainer hardware I used.
After moving back home, I sought to revive this technology and improve upon it so it could be shared with others.
Above: link to FlightGear
Notes: TBI
Quiz follows for three reasons
Ohio PEs that watch a webinar to attain CEUs are
required to pass a quiz
A quiz identifies what I hope you learn
I am envious of other professionals to attain CEUs
at this conference
Lately, I concentrate on improving my cycling cadence
Plus, my mind improves: I use mental energy to complete virtual flights.
If nothing else, it is more interesting to hear about my virtual flights than my time on the bike trainer

## Slide 2
This presentation is publically available on github:
https://github.com/toddwestley/Arduinos-to-turn-equipped-bike-into-Joystick-with-throtle-axis so you can go view the slides again.
Summary: In my humble opinion, riding a bike trainer is mind numbing.
Playing a flight simulator (without warping time) is equally mind numbing.
In combination, they lead to a palatable activity for me.
Notes: What time warping?
1 hour flight could only require 15 minutes

## Slide 3
Details: Playing a flight simulator with a joystick with a throttle axis is better than
just using a keyboard and mouse.
Throttle axis
Notes: I enjoyed playing FlightGear so I purchased a flight stick…
That was not satisfactory to me

## Slide 4
Details: What if a bike on a trainer could be used to control the throttle axis?
Bike on trainer; sweat guards in place.
Sweat guards prevent corrosion.
I have already replaced the bottom bracket twice!
Notes: I try not to sweat;
Sweat guards prevent damage to your bike

## Slide 5
Details: How could could the speed sensor on the rear wheel be used?
Speed sensor
A speed sensor is required! Above is a link to Amazon.com
Notes: Amazing to me, I kept an o-ring from years ago (when I worked with hydraulic crimp tools for plumbing systems, I think) that was ideal for sensor installation on my rear wheel ultegra hub
Initially, the sensor only work with a cell phone app. But, again, I was not satisfied. I knew I could do better.

## Slide 6
Details: When the wheel is spinning, the speed sensor transmits, with blue
tooth low energy, information on the total number of spins and angular
speed of the last spin.
Here is an 8 byte transmission (that occurs every second unless the
speed sensor stops spinning for 2 minutes) [going forward, the
transmitted information will be referred to as rawValue]:
1 ,5 ,16 ,0 ,0 ,182 ,82 ,0
The total number of rotations is the sum of
The “last event”
8
182+20992=21174
5+4096+0+0=4101
Notes: 8 bits to a byte…
I think the transmission is in reverse IBM form

## Slide 7
Details: Capturing this stream of bytes filled the programming space of an Uno
WiFi Rev2 Arduino
A second Arduino is required.
Note: The BLE signal from the speed sensor must be read by a sensor no
more than arms length away.
Notes: 2nd Arduino Leonardo acts as the joystick…
Source code available on github.

## Slide 8
What is an Arduino?
From “opensource.com”:
In a nutshell, an Arduino is an open hardware development board that can be used by tinkerers, hobbyists, and makers to design and build devices that interact with the real world.
Notes: Here is a description of an Arduino

## Slide 9
Details: These 8 bytes of information are transmitted via the wire interface
(using the ground, SCL [serial clock], and SDA [serial data] pins) to an
Arduino Leonardo that can act as joystick.
Notes: Leonardo and Uno Wifi Rev2 shown. Note the wires to channel information from the uno to the leonardo
I am not gifted at physical skills…this is the way I use it.

## Slide 10
Details: Formulas used in the Arduino programs I authored include:
Constants
“RawValue” description
Speed calculation
Joystick throttle axis position calculation
Notes: What follows in math intense….It took me 6 years to get here.

## Slide 11
based on the type of tire. This for a 700CC X 22mm road tire
This the highest speed you could theoretically obtain after operating the trainer for a long time
You pick this constant…help follows
This is the highest resolution possible
Notes: Constants
Wheel circumference can be found internet.
Note: I try to state units explicitly – this is a trick I used to pass the PE examination by eliminating answers on the multiple choice portion of the test.

## Slide 12
previous
Notes: Total rotation from rawValue

## Slide 13
or
Notes: Speed calculation
Delta wheel event must be positive

## Slide 14
*speedDelta+maxSpeed
Notes: Joystick throttle position calculation

## Slide 15
This is nerdy, and I am pretty sure the Arduinos are working even if their serial outputs are not visible, but, I like to know they are working (and how hard I am working the bike) while playing FlightGear so I wrote this Linux script.
You can also use the serial monitor on Arduino IDE to view the output from the Arduino Leonardo.
Notes: I use Linux; it should be possible to do this on Windows.

## Slide 16
How are SpeedGradient, SpeedDelta, and MaxSpeed defined?
I found something that worked for me…. Below is a link to a spreadsheet
You can adjust the parameters in cells L2:L3 see how they impact an actual ride (blue dots) from their use (red line). You can copy the contents to a new sheet and replace data in column A from one of your actual rides.
Notes: I made an Excel worksheet so you can determine your own Speed Gradient, SpeedDelta, and MaxSpeed.

## Slide 17
Details: Why use an exponential function?
Think of your effort on the bike trainer as a stream of water. Think of
your bike trainer as a tank for that water. That tank has a small hole at
the bottom. Water leaves that tank at a rate proportional to its height. As
time goes on, the tank will reach a constant level. That water (trainer
temperature) represents the resistance of your trainer. As time passes, the
resistance decreases and you pedal faster. This produces a differential
(i.e. difficult) equation whose solution includes an exponential function.
https://www.youtube.com/watch?v=-1ARYph3mNA
Notes: I used a high school junior to help me solve a differential equation equivalent to understanding water flow into a tank (with constant cross-section) with a hole at its bottom.

## Slide 18
Quiz:
An Arduino is?
A. Small lizard indigenous to Northern Mexico
B. Hardware development circuit board
C. An alternative to salt-peter
D. Slang for a nerdy middle school student
The stream of data from a speed sensor is made up of how many bytes every second?
A. 8
B. 1
C. 64
D. 2
How many Arduinos did Todd use to transform a bike trainer into a joystick throttle axis?
A. 0
B. 1
C. 2
D. 16
What pins are used by the Arduino “Wire” library
A. SDA
B. SCL
C. Ground
D. All of the above

## Slide 19
Quiz:
At most, how manty bytes of the speed sensors’ transmission are used by Todd’s Arduinos every second?
A. 64
B. 6
C. 7
D. 8
How many bytes comprise the “last event” evaluation to determine cycling speed?
A. 2
B. 4
C. 8
D. 12
Who determines when it is necessary to operate the bike’s shifters?
A. The end user decides.
B. The end user is given suggestions by the Arduino.
C. The Arduino wire library dictates this to the cyclist
D. The shifters operate through BLE

## Slide 20
Quiz:
According to Todd, using a bike trainer by itself is:
A. Mind-numbing
B. Exhausting
C. Critical for improving short-term strength
D. Furniture, similar to a couch
The units of “speed gradient”, if distance traveled is miles, are:
A. millimeters
B. miles per hour
C. miles
D. unit less
The exponential function used by Todd to determine what the cyclists’ speed should be is:

## Slide 21
I am in debt to the Holy Spirit for gently encouraging me to move forward on this project.
If you are moved, please make a donation to:

## Slide 22
Thing left to do:
add slides to show how to define speedDelta, maxSpeed, speedGradient
what is an Arduino?
make a quiz
make a box for Arduinos
order USB cables
email Bryan Pugh about presenting next year
offer CEUs to other PEs
oring for speed sensor
Can spread sheet be embedded in Windows 8?