## Slide 1
https://www.posthope.org/team-todd

## Slide 2
Todd resided here
Justification Why Todd is Presenting
Notes: This article describes how I got my brain injury.
Note: I lived in Ohio at the time

## Slide 3
I have been a cyclist since college:
Completed
200 km ride around European Lake Constance
while I worked in Switzerland for 6 months.
Cyclist on relay team that won a Triathlon
In Vermillion Ohio
Lake Constance
Presentation Background
Notes: Thank you…
Background – I have been riding since I was 20.

## Slide 4
This presentation is publically available on github:
https://github.com/toddwestley/Arduinos-to-turn-equipped-bike-into-Joystick-with-throtle-axis so you can download these slides.
Search on google for “toddwestley site:github.com”
Presentation Publicly Available
Notes: Link to slides; I mispelled throttle; google search for ‘toddwestley site:github.com”
This presentation is about two boring activities: riding a bike trainer and playing a flight simulator.
  Combining them rendered an enjoyable activity -- In spite of disability, I still can enjoy cycling.
  Lots of hyperlinks in this presentation.

## Slide 5
Went airshow in Oshkosh, WI with Uncle Steve when I was young.
When I was older, I worked on Steve’s project to build Piper Cub from plans.
EAA
How Todd Got Involved in Aviation
Notes: Went to air show in Oshkosh Wisconsin with Uncle Steve
After college, he started building a Piper Cub from plans

## Slide 6
Initially, bike trainer to flight stick throttle innovation required elevated privileges.
More of Todd’s Aviation Background
Notes: Flying without flight lessons or a pilot’s license is not unheard of. I thought I should be at least by at least familiar with a piper cub aeronautical characteristics.
Who can tell me the names of two people who flew without single a lesson?
I maintained my cycling abilities while living in the NE Ohio by riding a bike trainer.
I combined them and translated rear tire speed into a throttle position.

## Slide 7
My configuration worked for me; but, no one knew about the bike trainer hardware / software I used.
After moving back home, I sought to revive this technology and improve upon it so it could be shared with others.
Above: link to FlightGear
FlightGear
Notes: I shared my habit with few; When I started to live at my parents home …. I wanted to virtually fly again
I included a link to FlightGear on this slide.

## Slide 8
Details: Playing a flight simulator with a joystick with a throttle axis is better than
just using a keyboard and mouse.
Throttle axis
Throttle Axis
Notes: I enjoyed playing FlightGear so I purchased a flight stick…
  That was not enough to me

## Slide 9
Details: I knew a bike on a trainer could be used to control the throttle axis.
Bike on trainer; sweat guards in place.
Sweat guards prevent corrosion.
I have already replaced the bottom bracket twice!
Bottom bracket
Todd’s Bike on a Trainer
Notes: I wanted to use my bike on the trainer again
  Here is my bike on a trainer…
  I try not to sweat; body sweat corrodes bottom bracket
  Sweat guards prevent damage to your bike
  I now take improved protective measures: I use fans to blow the sweat away now.
  This is the bike in our basement

## Slide 10
Details: How could the speed sensor on the rear wheel be used?
Speed sensor
A speed sensor is required! Above is a link to Amazon.com
Speed Sensor Close-up
Notes: Initially, the sensor only work with a cell phone app. But, again, I was not satisfied. I knew I could do better. I captured its data with a R Pi.
  Then on my linux desktop, and finally the Arduinos
I still wanted to share my quirk with Windows users.

## Slide 11
Details: When the wheel is spinning, the speed sensor transmits, with blue
tooth low energy, information on the total number of spins and angular
speed of the last spin.
Here is an 8 byte transmission (that occurs every second unless the
speed sensor stops spinning for 2 minutes) [going forward, the
transmitted information will be referred to as an array of 8 unsigned bytes called rawValue]:
1 ,5 ,16 ,0 ,0 ,182 ,82 ,0
The total number of rotations is the sum of
The “last event”
8
182+20992=21174
5+4096+0+0=4101
Total rotations
Last Event Time
Reverse IBM form
Math Used by Arduino Leonardo
Notes: The Wahoo sensoir transmits 8 bytes every second
I learned this while using a linux based Raspberry PI – I use linux OS; not Windows. But my scheme still works for Windows users.

## Slide 12
Details: Merely, capturing this stream of bytes filled the programming space of an Uno
WiFi Rev2 Arduino.
A second Arduino is required.
Note: The BLE signal from the speed sensor must be read by a sensor no
more than arms length away.
Important to remove power from this Arduino after each ride,
        Otherwise it will continue to deplete the battery of the speed sensor
Programming Space Full
Notes: Program storage space of Uno WIFI rev 2 filled
2nd Arduino Leonardo acts as the joystick…
Source code available on github.

## Slide 13
From “opensource.com”:
In a nutshell, an Arduino is an open hardware development board that can be used by tinkerers, hobbyists, and makers to design and build devices that interact with the real world.
What is an Arduino?
Notes: Here is a description of an Arduino

## Slide 14
Details: These 8 bytes of information are transmitted via the wire interface
(using the ground, SCL [serial clock], and SDA [serial data] pins) to an
Arduino Leonardo that can act as joystick.
Leonardo
Uno Wifi Rev2
Arduino In Use
Notes: Leonardo and Uno Wifi Rev2 shown. Note the wires to channel information from the uno to the leonardo
I am not gifted at physical skills…this is the way I use it.

## Slide 15
Source: https://en.wikipedia.org/wiki/Flight_control_surfaces
Besides the throttle, there are other controls:
keyboard
surface trim tab
  Bank aileron A 4,6 :,”
  Pitch elevator C 2,8 1,7
  Yaw rudder D - -
Auto-coordination between rudder and aileron in use
Keystrokes will be shown in upper left corner of this
screen during flight
Aircraft Control Surfaces
Notes: Here is an illustrations of the controls I use while flying.

## Slide 16
Todd’s email: toddwestley@gmail.com
Some details in the Arduino code that I concede are mathy:
  Constants
  SpeedGradient, SpeedDelta, MaxSpreed
  Using spreadsheet to determine speedGradient, speedDelta, maxSpeed
Todd’s Email Address
Notes: Trainer resistance abates as it is used. How was this accounted for?
This is intended for those that want to understand details of how I transformed my bike.

## Slide 17
based on the type of tire. This for a 700CC X 23mm road tire
This the highest speed you could theoretically obtain after operating the trainer for a long time
You pick this constant…help on this follows on the next slide
This is the highest resolution possible
Constants
Notes: Constants
Wheel circumference can be found internet.
Note: I try to state units explicitly – this is a trick I used to pass the PE examination to eliminate incorrect answers on the multiple choice portion of the test.
I embedded a spreadsheet to use the serial output from you riding your bike on a trainer, to calculate your speedGradient.

## Slide 18
How are SpeedGradient, SpeedDelta, and MaxSpeed defined?
I found something that worked for me…. Below is a link to a spreadsheet
You can adjust the parameters in cells L2:L3 see how they impact an actual ride (blue dots) from their use (red line). You can copy the contents to a new sheet and replace data in column A from one of your actual rides.
SpeedGradient, SpeedDelta, MaxSpreed
Notes: I made an Excel worksheet so you can determine your own Speed Gradient, SpeedDelta, and MaxSpeed.

## Slide 19
Using spreadsheet
Copy existing sheet into a new sheet
Delete existing serial output
Paste the serial output of your ride into the sheet!
The blue dots are your actual ride
Adjust the parameter in cell L15 until the green dots match the blue dots
Adjust parameters in cells L2:L4 until the red dots are just above blue dots

## Slide 20
I put a lot of thought into how this works.
This diversion brought back the enjoyment of cycling to me. It brought variations from winds, temperatures, and altitude into the basement.
I also enjoy programming and relearning math
It’s not about physical fitness although that is a side effect. The activity, I believe, also led to a low resting heart [bradycardia] rate (<52 bpm).
Questions?
Questions
Notes: When you watch me fly from KGAI to KBWI, I do not translate linearly from a Maximum speed to throttle position: I use more math and account for the trainer’s decrease in resistance from use.

## Slide 21
Questions?
And/or
Watch Todd fly virtually from KGAI to KBWI [About 16 minutes]
Justification Why Todd is Presenting
Presentation Background
Presentation Publicly Available
How Todd Got Involved in Aviation
More of Todd’s Aviation Background
FlightGear
Throttle Axis
Todd’s Bike on a Trainer
Speed Sensor Close-up
Math Used by Arduino Leonardo
Programming Space Full
What is an Arduino?
Arduino In Use
Aircraft Control Surfaces
Todd’s Email Address
Constants
SpeedGradient, SpeedDelta, MaxSpreed
Using spreadsheet
Notes: Questions?

## Slide 22
What I did to present:
  Wrote a batch file:
    cd E:\CoolTermWin64Bit
    start coolTerm.exe e:\coolTermWin64Bit\connection_settings_zero.stc
    arduino.exe"
    cd /d E:\ShowOff
    start Showoff.exe
    cd /D "C:\Program Files\FlightGear 2020.3\bin"
    start /high fgfs.exe --launcher
  Used CoolTerm to display Arduino Leonardo serial output
  Used ShowOff to show user inputs in upper left of screen
    https://www.dcmembers.com/skrommel/download/showoff/
  Arduino.exe reports serial output of Arduinos
Presentation Mechanics
Notes: Show displays key strokes in upper left
  NumPad 7 and Numpad 1 are elevator trim
  Numpad 9 and Numpaf 3 are throttle
CoolTerm record text output from Arduino
  Text output corresponds to throttle position
  Distance gives me a clue if it is too early to shift
  I like to record the text output – I am nerdy!

## Slide 23
Heading
Altitude above ground
Altitude above sea level
Rudder (auto-
coordination
in use)
GPS destination
Throttle
Air speed (knots)
Aileron (and trim)
Elevator (and trim)
Glide slope
Pre-flight briefing
Pre-flight Briefing
Notes: Here is the Heads Up Display I look at…
  GPS, throttle, air speed, aileron (and trim), elevator (and trim), rudder, heading, altitude above ground, altitude above sea level
  I takes about two minutes for the software to start running
  The flight from Gaithersburg to BWI takes about 16 minutes.
  I like to know the aircraft can still get airborne after lands
    Center control surfaces and then take off

## Slide 24
I am in debt to the Holy Spirit for gently encouraging me to move forward on this project.
If you are moved, please make a donation to:

## Slide 25
Video of a flight
Video of Todd on a Trainer

## Slide 26
What will Todd use to exhibit this feat?
8020 structure to hold plank
Plank
  Mouse
  Mouse Pad
  Mouse Pad support
  Keyboard
  Cover for key board
Structure for Arduinos
  Arduino Leonardo
  Arduino Uno Wifi Rev 2
  Tupperware to hold Arduinos
  USB hub
  USB Type B cable for Uno Wifi Rev2
  USB cable for Leonardo
  3 wires for Arduino communication
Front wheel support and board to raise whl. spt.
Bike Trainer
Bike (not shown; with speed sensor)
Fans (not shown)
Screen (not shown)
PC (not shown)

## Slide 27
Starter list
Todd’s list
8020 structure to hold plank
Plank
  Mouse
  Mouse Pad
  Mouse Pad support
  Keyboard
  Cover for key board
Structure for Arduinos
  Arduino Leonardo
  Arduino Uno Wifi Rev 2
  Tupperware to hold Arduinos
  USB hub
  USB Type B cable for Uno Wifi Rev2
  USB cable for Leonardo
  3 wires for Arduino communication
Front wheel support and board to raise whl. spt.
Bike Trainer
Bike (not shown; with speed sensor)
Fans (not shown)
Screen (not shown)
PC (not shown)
Ironing board
Plank
  Mouse
  Mouse Pad
  Mouse Pad support
  Keyboard
  Cover for key board
Structure for Arduinos
  Arduino Leonardo
  Arduino Uno Wifi Rev 2
  Tupperware to hold Arduinos
  USB hub
  USB Type B cable for Uno Wifi Rev2
  USB cable for Leonardo
  3 wires for Arduino communication
Front wheel support and board to raise whl. spt.
Bike Trainer
Bike (not shown; with speed sensor)
Fans (not shown)
Screen (not shown)
PC (not shown)
Notes: I would not omit the items greyed out; you could though

## Slide 28
What if my laptop computer has bluetooth already!
  Linux  Great: I already wrote software (modified gatttool)
          SUDO required each time the software is executed
  Windows  I wrote software that Google suggests got a virus
          Software written in VisualStudioCode : 20 Gigabyte download

## Slide 29
Possible questions:
  Did you make a quiz so Ohio PE’s could earn a CEU?
  Can you better illustrate/explain the math involved?
    Could have used a Laplace transform?
  Can you explain the parameters that dictate the throttle position?
  Did you know trainer resistance fades during their use? Did you take this into account?
  How do turn on/off the glide slope indicator?

## Slide 30
How can I do this?
  Get a trainer, Wahoo sensor, Arduino Leonardo, Arduino Uno Wifi Rev2
    You may want a 60mm OD x 3.5mm wide o-ring
    Get at least a something to absorb your sweat
    Get bike trainer
  Program the Arduinos
  Make a desk to go over your bike on the trainer
    Buy keyboard and water shield for the keyboard
  Learn the MAC address of your Wahoo sensor
    Use cell phone App LightBlue
  Rewrite the code of the Arduinos
    You need the MAC address for the Uno Wifi Rev2
    You need to set you parameters for Leonardo code
      There is a spreadsheet embedded to help you
      Ride the trainer for a exercise period of choice (I used 1 hour)
  Learn to use flight simulator
    KTTS in Florida is a 3 miles long by 300 feet wide!
  Post your questions on GITHUB and I will answer them there.

## Slide 31
What I did to present:
  Wrote initial conditions for FlightGear:
    --enable-terrasync
    --fov=54.4
    --enable-auto-coordination
    --disable-clouds
    --visibility=39496
  Modified keyboard XML:
--enable-terrasync
--fov=54.4
--enable-auto-coordination
--disable-clouds
--visibility=39496

## Slide 32
Details: This is very math centric…Formulas used in the Arduino programs I authored include:
Constants
“RawValue” description
Speed calculation
Joystick throttle axis position calculation
Notes: What follows in math intense….It took me 6+ years to get here. Frankly, I would have reviewed this presentation numerous times if it had been available.

## Slide 33
This is nerdy, and I am pretty sure the Arduinos are working even if their serial outputs are not visible, but, I like to know they are working (and how hard I am working the bike) while playing FlightGear so I wrote this Linux script.
You can also use the serial monitor on Arduino IDE to view the output from the Arduino Leonardo.
Notes: I use Linux; it is possible to do this on Windows.

## Slide 34
Details: Why use an exponential function?
Think of your effort on the bike trainer as a stream of water. Think of
your bike trainer as a tank for that water. That tank has a small hole at
the bottom. Water leaves that tank at a rate proportional to its height. As
time goes on, the tank will reach a constant level. That water (trainer
temperature) represents the resistance of your trainer. As time passes, the
resistance decreases and you pedal faster. This produces a differential
(i.e. difficult) equation whose solution includes an exponential function.
https://www.youtube.com/watch?v=-1ARYph3mNA
Notes: I used a high school junior to help me solve a differential equation equivalent to understanding water flow into a tank (with constant cross-section) with a hole at its bottom.
I put much thought into using a decaying exponential function.

## Slide 35
I am in debt to the Holy Spirit for gently encouraging me to move forward on this project.
If you are moved, please make a donation to:

## Slide 36
Thing left to do:
add slides to show how to define speedDelta, maxSpeed, speedGradient
what is an Arduino?
make a quiz
make a box for Arduinos
order USB cables
email Bryan Pugh about presenting next year
offer CEUs to other PEs
oring for speed sensor
Annex
What I did to make flightgear run on Windows two – DLLs
vcruntime140_1.dll
msvcp140.dll
Windows CoolTerm vs Linux script to record Serial Output of Leonardo
Comparison of joystick set up
spellung error on github

## Slide 37
Cost Analysis for potential end user
Assumptions: Potential users have a bike only and will consider Windows 10 PC only.
Amazon or McMasterCarr will be sole source of products
Potential users have space for this stuff:
Trainer stand 34.99
Desktop PC w/ Monitor 131.50
Arduino Leonardo w/cable 14.99
Arduino Uno Wifi Rev2 (abx00021) 54.96
Wahoo Speed Sensor 39.99
Fan 39.99
4 port USB port w/ power switches 16.95
Keyboard cover *must match PC’s keyboard! 13.99
Trainer Sweat Guard 9.99
80/20 Material to make shelf to go over handle bars 234.75 Arduino Jumper Wires [you should be able to find these!] 1.99
USB cable for Arduino Uno 6.99
Total 651.08+shipping
Green from McMaster Carr

## Slide 38
234.75

## Slide 39
Wow, $651.08 + shipping! I thought Todd had a fixed income.
I rode a trainer stand, prior to Oct 29, 2014. After that day I rode that a trainer stand for a few weeks before I severed the shaft leading to the trainer stand’s fly wheel. I also used that trainer to control the throttle axis with a USB-1208LS. I already had an affinity for the Linux PC I have – I was frugal and liked to program.
Arduino are open source and appeal to hobbyists: I challenge you to find a more economical alternative.
Cheaper ANT+ speed sensors are available. I am unwilling to deviate.
In Elyria, I kept my apartment at 55°F – the furnace was loud; the lease did not allow me to go lower. When I moved back home, other residents preferred a warmer temperature. I try not sweat.
I did not know how to find a shelf: I built one from materials I knew about. Surely you can find a cheaper alternative.
From the USB-1208LS, I had a type B USB cable for the Arduino Uno Wifi Rev2
I have oodles of jumper wires: if you need some, come by my residence and I will give you some.

## Slide 42
Comparison of Joystick configurations – Windows, Microsoft takes credit.

## Slide 43
Comparison of Joystick configurations – Linux, Arduino LLC takes credit

## Slide 44
What I did to make FlightGear run on Windows – two missing DLLs
vcruntime140_1.dll -- followed instructions on YouTube
msvcp140.dll -- found on hard drive and copied
into FlightGear directory
If I did this over again, I would install and run CoolTerm first, then FlightGear

## Slide 45
I like to see and have a record of the Serial Output from the Leonardo. On linux, I use this script file
[batch file]:
PREFIX=Arduino_from_20
SUFFIX=.txt
TIMEDATENOW=$PREFIX$( date +%y_%m_%d_%s)$SUFFIX
stty -F /dev/ttyACM0 raw 9600
cat /dev/ttyACM0 2>&1 | tee $TIMEDATENOW
The same can be accomplished on Windows by using CoolTerm…

## Slide 46
Download and install coolterm
launch cool term
click options
Select Leonardo port
you can learn this from the
Arduino IDE
Click fonts
change font size to as desired

## Slide 47
Click connection menu >> capture to Text/Binary File >> start

## Slide 48
Select a name as prompted…
Click connect
Plug USB cable into Uno Wifi Rev 2 Arduino (this causes the Arduino to restart)
Start FlightGear, select departure airport, etc. …get past launcher,
after cockpit is visible… Start pedaling – Serial Output data will appear,
When ride is complete…
Unplug the Uno Wifi Rev 2
Connection >> Capture to Text/Binary File >> stop
Disconnect Serial
Quit – Don’t save settings
If desired, analyze the ride to (Select topSpeed, deltaSpeed, and speedGradient)

## Slide 50
@echo off
cd E:\CoolTermWin64Bit
start coolTerm.exe e:\coolTermWin64Bit\connection_settings_zero.stc
cd E:\ShowOff
start Showoff.exe
cd E:\FlightGear 2016.4.4\bin
start fgfs --launcher
exit
startApps batch file used
Notes: How I would capture serial output…
I used flightgear 2016 so flightgear would fit on a jump drive.
On coolTerm, don’t forget to <ctrl> r to start recording.

## Slide 52
This presentation is publically available on github:
https://github.com/toddwestley/Arduinos-to-turn-equipped-bike-into-Joystick-with-throtle-axis so you can download these slides.
Search on google for “toddwestley site:github.com”
Summary: In my humble opinion, riding a bike trainer is mind numbing.
Playing a flight simulator (without warping time) is equally mind numbing.
In combination, they lead to a palatable activity for me.
        I discovered that I could play games in plain sight of those around and they incorrectly conclude the activities are only exercise.
        I now can plan the nature of my exertions, i.e. how fast can I climb that hill?, and include variations from real world weather.
        This presentation is about my quirky leisure activity.
Notes: Link to slides; I mispelled throttle; google search for ‘toddwestley site:github.com”
This presentation is about two boring activities: riding a bike trainer and playing a flight simulator.
  Combining them rendered an enjoyable activity -- In spite of disability, I still can enjoy cycling.
  Lots of hyperlinks in this presentation.

## Slide 53
It all began when my Uncle Steve was building a Piper cub from scratch while I lived in Ohio. In the winter, it was too cold for me to ride my bike outside. I rode a trainer, but it was boring. Than I decided to couple that with playing a flight simulator that had a piper cub aircraft. I used as USB-1208LS to capture the “:speed” of my rear wheel and my PC translated that into a throttle position. At that point, I got in the habit of virtually flying.

## Slide 55
Hamm’s suggestions
  Header each slide
  Should url of presenation go first
  Why did you want to control a simulator with you bike
  Speed sensor picture; bottom bracket picture
  Picture of Todd on the trainer

## Slide 56
previous
Rotations Math
Notes: Total rotations from rawValue

## Slide 57
or
Speed Calculation
Notes: Speed calculation
Delta wheel event must be positive

## Slide 58
*speedDelta+maxSpeed
Throttle Position Calculation
Notes: Joystick throttle position calculation
  Note the exponential function used – this accounts the lack of resistance as the trainer is used.